## Slide 1
Presentation by Yi-Chih Tung
Chapter 7
Calling Convention
In order for compilers, assemblers and linkers to produce a final working executable, an agreement must exist between them on the use of the stack and the registers used. Since we're using the GNU compiler collection in this course, let's discuss the GNU calling convention.

## Slide 2: Register Usage
One of the first considerations of the convention is the use of available registers and who's responsible for saving and restoring them. Registers are limited in number and sometimes have architectural limitations.
RISC-V restricts us to using registers x1 to x31, since x0 has a hardwired zero or discard talent. The remaining registers are fully general purpose.
The above table lists the registers that are available, their intended function and who saves them when necessary.

## Slide 3: Call Procedure
In order for a subroutine to return to the caller where it left off, a return address must be provided as part of the call. In RISC-V this is performed by the Jump and Link "jal" or the Jump and Link Register "jalr" instructions:
Opcode jal
The "jal" instruction permits the programmer to code a "call" to a subroutine. It performs two things when it executes:
1. Copies the current PC + n, which is the address following the current instruction, to the destination register rd.
2. Adds the relative o set to the address PC + n to begin execution at the called location.

## Slide 4
Pseudo Opcode jr
In order to return from the call, the "jr" pseudo-opcode can be used to return to the address found in the specified register.
jr rs
The operation of this instruction sets the PC to the value in register rs.
jalr x0,rs,0
Pseudo Opcode ret
The "ret" is a pseudo-opcode that is expanded by the assembler into:
jalr x0,ra,0
Call to 32-bit Absolute Address
The "call" pseudo-op comes to the rescue for calling, for example, a function named foo:
call rd, foo # specified rd register, or...
call foo # ra (x1) is assumed
This pseudo-op is expanded into a pair of instructions "auipc" and "jalr" to accomplish the far call. The expansion of the normal case of "call foo", would be:
1: auipc ra,%pcrel_hi(foo)
jalr ra,ra,%pcrel_lo(1b)

## Slide 5: General Call Procedure
1. The caller performs a "jal" or "jalr", causing the return address to be placed in rd, which is normally ra (x1).
2. The PC jumps to the offset + rs to start executing the called code.
3. The called code, returns by "ret", or "jr ra", or "jalr x0,ra,0".
Revised Call Procedure
1. The caller performs a "call", causing the return address to be placed in rd, which is normally ra (x1).
2. The PC jumps to the subroutine address to start executing the called code.
3. The called code, eventually returns by "ret" (or "jr rs", when a different register is used).

## Slide 6: Concrete Call Example
In this example, we're going to call function foo(), which is assumed to be far away from the caller's current PC. In the fol lowing, the PC for the "auipc“ instruction is 0x42005e16
verify this calculation using gdb:
Notes: The current address of the "auipc" instruction
0x42005e16 is added to the constant 0x7EA000 (which
is derived from 0x7EA placed in the upper 20 bits) and
the result is tem porarily stored into ra (x1). Then the
"jalr" instruction adds the constant 490 (decimal) to ra
(x1), to arrive at 0x427F0000 for foo(). As part of the
"jalr" instruction, the return ad dress of 42005E1A + 4 is
now stored into ra (x1), while the PC register is set to
foo's entry point address of 0x427F0000.

## Slide 7: Simple Call Experiment
1. Loads the value of 1 into the register a0 (x10) in line4.
2. Calls an internal subroutine named "intern" from line5, using temporary register t0 (x5).
3. Adds the value 2 to the value in a0 in line 8.
4. Returns to the caller from line 9, via register t0 (x5), to line 6.
5. Control returns to app_main() from line 6, using register ra (x1).
~/riscv/repo/07/jal/main/main.c.
build and flash this code, the run output should report the following
This is the expected return value (1 + 2).

## Slide 8: The same program exists for QEMU. build and run it as follows:
$ cd ~/riscv/repo/07/jal/qemu64
$ gcc -O0 -g jal.S main.c
$ ./a.out
Running in gdb – fedora riscv qemu

## Slide 9
$ gdb ./a.out
with the "list" command:
let's set a "breakpoint" for the function callme():
(gdb) b callme

## Slide 10: Since the program is not running yet, let's start it: (gdb) r
Notes: Because we have the breakpoint set, the execution
paused as soon as it entered the as sembler routine
callme().
Now we can trace one instruction at a time. Let's "step"
one instruction:
(gdb) s
We see the execution has performed the assembler
statement of line 4. But let's examine the register contents
of a0

## Slide 11
Let's step one more instruction:
we've called the intern() function by use of t0. Step once again and display registers:
register a0 now has the value 3, and the register t0 has
the return address from the call in line 5. Let's step from
line 9:
From this, we see the control has returned to after the
point of the call in line 6. Stepping once again should get us back to the main() program,
we see that the printf() call was also completed as part of the return, so that gdb could return a complete statement executed, returning to the statement following in line 9.
Since we don't care about tracing the rest of the program
you can just "continue" it as follows
The program then exits in the normal way

## Slide 12: Argument Passing in Registers
Arguments are passed in registers starting with a0 (with exceptions for hardware floating point). And that return values are returned starting with a0. Arguments and return values less than or equal to XLEN bits in size are sign-extended into the register for signed types.
Figure below illustrates how a long long int is passed or returned for the ESP32-C3

## Slide 13
The Stack
The stack pointer value is found in register sp (x2) and is set to the high address of the stack and grows downward.
The stack pointer is maintained at an alignment boundary, which for ESP32-C3 (where XLEN=32) is a double word address (modulo 8 bytes). For XLEN=64 platforms (QEMU), this is modulo 16 bytes.
Prologue
At the start of the function, the prologue serves to perform any functions necessary to preserve the integrity of the call.
The general procedure is:
1. Decrement sp by the stack frame size for register saves, including any local variable space (the size is round up to mod 8 for XLEN=32, or mod 16 for XLEN=64).
2. Store registers to be saved in the allocated stack frame (this optionally includes the s0/fp (x8) register).
3. Save register ra (x1) when the called routine calls or reuses register ra.

## Slide 14
Epilogue
When it is time to return to the caller, the stack changes must be undone, and the necessary registers restored.
This procedure consists of:
1. Reload saved registers (including optional s0/fp).
2. Reload ra (if necessary).
3. Increment sp by the amount it was subtracted in the prologue.
4. Return to the caller's address in register ra.
Floating Point Arguments
When floating-point hardware is supported, they are passed in floating-point registers fa0 to fa7 similar to the way that integer values are passed.
Returned floating-point values are returned in fa0.
When the floating-point data type is handled by software, those values are passed in the usual integer registers instead.

## Slide 15: A Big Call Experiment
Let's exercise a C main program calling the assembler routine bigcall(), with nine arguments of type int32_t and int64_t using the ESP32-C3.
Program - ~/riscv/repo/07/call/main/bigcall.S, assembler module for bigcall().

## Slide 16
~/riscv/repo/07/call
Build, flash monitor
Success!

## Slide 17: Calling printf()
Main program, ~/riscv/repo/07/bigcall2/main/main.c ESP32-C3.
The program illustrated in Listing 7.6 is much the same as before with the following changes:
1. Line 36 moves the sum to register a1, to act as a second int argument to the printf() call.
2. Line 40 uses the pseudo-op "la" to load an address into a0. This is the pointer to the format string to be passed to printf().
3. Line 42 calls printf(), with the arguments in registers a0 and a1. Recall that the call (by default) clobbers register ra (x1) with the printf() return address, which is why the register was saved in the function prologue.
4. Line 43 handles the value returned by printf(), and saves it in our stack variable var1. We don't actually use it here but it demonstrates the use of a stack-based variable.
5. Lines 52 and 53 defi ne the printf() format string in a read-only section used for literals.

## Slide 18
~/riscv/repo/07/bigcall2
Build, flash monitor

## Slide 19: Thank You !