## Slide 1
Presentation by Yi-Chih Tung
Chapter 8
Flow Control
This chapter examines some fun programs to exercise branching instructions. Branching is a fundamental part of a loop, which allows repeated operations.

## Slide 2: Branching Instructions
The RISC-V documents like to refer to these as control transfer instructions. Of these, there are two basic categories:
• Unconditional transfers
• Conditional branches
Conditional Branches
With conditional branches, the comparison and the branch are combined into one opera tion. The following are signed comparison branches (the operation in C language terms is provided in the comment):

## Slide 3: Unconditional Transfers
We've already seen the "jal" and "jalr" opcodes for calling a subroutine. When the destination register is set to zero/x0, either explicitly or by a pseudo-op like "j", they become simple unconditional transfers because there is no return address produced. The "jal" and "j“ opcodes have the ability to jump +/- 1 MB from the current program counter (pc) since the o set is encoded as a signed half-word o set. The "jalr" opcode on the other hand encodes the o set as a 12-bit signed byte o set and therefore has a more restricted range.
The following are variations of the unconditional transfer. For easy-to-read code, the "j" or "jr" pseudoopcodes are recommended:

## Slide 4
Shift Opcodes
In the C language, you often don't consider whether it involves a logical or arithmetic shift operation. That is because it is determined by the data type. When unsigned, it requires a logical shift. When signed, it requires an arithmetic shift, when shifting right. The arithmetic right shift preserves the sign while the remaining bits are shifted right. All shift-left operations are logical shifts, which is why you don't see a "sla" opcode. Logical shifts always populate the shifted-out bit position with a zero.
RV64I Shift Opcodes
In addition to the previous shift opcodes, RV64I adds these:

## Slide 5: ESP32-C3 Project
In this project, we'll write both an optimized C language program and an assembler language equivalent to count the number of 1-bits in a 32-bit integer, for the ESP32-C3. Let's then compare the two routines in this bake-o to see if the compiler can out-perform our assembly language code.
Function c_ones()
Listing 8.1 illustrates our test C language program, optimized at GCC level -O3 for good performance. The main program first invokes the assembler routine ones() in line 27 and saves the bit count in variable bcount. Then the C language function is called in line 31 with the returned value saved in variable count in Test Program
Main program with c_ones() function,
~/riscv/repo/08/ones/main/main.c.

## Slide 6
Assembler Function ones()
In this routine we ini tialize temporary register t0 with zero (line 3) then we drop into the loop starting at line 5.
There we test if the argument in a0 is already zero or has become zero.
Assembly language function ones(),
~/riscv/repo/08/ones/main/ones.S.
Run it
Build, flash and monitor the result from the ESP32-C3
device:
$ cd ~/riscv/repo/08/ones
$ idf.py build
This confirms that both the assembly language function and the C language functions agreed. Examination of the return values indicates that the results are correct.

## Slide 7
Routines Compared
$ ~/riscv/repo/listesp main/main.c
It's clear from this listing that the C compiler chose to generate this function a little di er ently than our own assembler routine.
Compare and Set As reviewed in the examination of the c_ones() function, the C compiler used the "slti" opcode to set the destination register to a 1 or a 0 based upon the result of a comparison. There are other compare and set opcodes similar to it.
These are listed with their C lan guage
equivalent expression in the comments:

## Slide 8: Odd Parity Example
Let's try another example, that is perhaps a little more practical. Our assembler routine named odd_parity() will determine if there is an odd or even number of 1 bits. The return value will be 1 if the parity is odd, else it returns 0 for even parity.
The odd_parity() function,
~/riscv/repo/08/parity/main/parity.S
The main test program,
~/riscv/repo/08/parity/main/main.c.
Build, flash and monitor this ESP32-C3 project as follows:
$ cd ~/riscv/repo/08/parity
$ idf.py build

## Slide 9: RV64I Odd Parity
Let's do a 64-bit version of the odd_parity() function.
Listing 8.7 lists the main program that drives this test. In this example, notice that odd_parity() now accepts a 64-bit integer argument for parity tests.
Main program listing,
~/riscv/repo/08/parity/qemu64/main.c.
Build and execute the program as follows in qemu riscv fedora
$ cd ~/riscv/repo/08/parity/qemu64
$ gcc -g parity.S main.c
$ ./a.out

## Slide 10: Position Independent Code
Normally we write code to execute at one fixed address. But what happens if the code needs to be copied to a different address and executed there? Traditionally, this requires fixing up addresses of referenced routines that didn't move. Under Fedora Linux, for example, shared libraries need to be able to run in the shared memory segments, which are dynamically allocated. This creates two problems:
1. Labels of instructions that move with the code, need to be relative to the pc. In this way, moving the code does not upset branch references because they remain relative to the current address.
2. Fixed labels of routines or global data that do not move, require some special treatment in order to remain valid after the move.

## Slide 11: Thank You !