## Slide 1
Presentation by Yi-Chih Tung
Chapter 9
Basic Opcodes
This chapter introduces a number of additional opcodes, which are the essential building blocks for most RISC-V assembly language programs.

## Slide 2: Arithmetic Opcodes
add, addi and sub
You've already used "add" and "addi", which simply add two values. Notice that there is no "subi" (subtract immediate) opcode. The same effect can be accomplished by adding a negative immediate constant.
Lui
The "lui" opcode provides a way to load 20 bits of unsigned data, into the high order 32 bits of a 32-bit register.
the instruction: lui a0,0xEEEEE results in a0 receiving the value of 0xFFFFFFFFEEEEE000 for RV64.
auipc
It adds the current location (register pc before it is incremented) to the unsigned immediate data (shifted up 20 bits). Like the "lui" opcode, bit 31 is sign-extended to the full register width for RV64 and larger platforms.
RV64 Arithmetic

## Slide 3: Logical Opcodes
The logical opcodes permit the programmer to perform bit-wise logical operations.
The operations of "and", "or" and "xor" should be familiar to the C/C++ language programmer.

## Slide 4: ESP32-C3 Rotate Left
Many microcomputer architectures support some kind of a rotate left or right instruction, which is noticeably
absent in RISC-V. But the example program in Listing
9.1 demonstrates that this really is no hardship. Function rotate_left() rotates an uint32_t integer left one bit, placing the shifted out bit into bit position 0.
Rotate left assembler function, ~/riscv/repo/09/rol/rol.S.
Main program from ~/riscv/repo/09/rol/main/main.c.
Modify , code in main.c
Add, #include <inttypes.h>
printf("rotate_left(0x%08" PRIx32 ") returned 0x%08"
PRIx32 "\n", bits, rol);
Build, flash and monitor the program as follows:
$ cd ~/riscv/repo/09/rol
$ idf.py build
Notes: At the end of the test run, the returned value is indeed
0xBEEF, which is the value that it started with. Success!

## Slide 5: RV64 Rotate Left
Under RV64, we have 64-bit registers to work with and Listing 9.3 illustrates a version of the same for running under QEMU. The only difference is the comment in line5 is modified to reflect 64 bits.
Program for rotate_left() function,
~/riscv/repo/09/rol/qemu64/rol.S.
The main program in
~/riscv/repo/09/rol/qemu64/main.c.
$ gcc -g rol.S main.c
$ ./a.out
The result shows proof positive that the rotate left was correct because the original value returned after 64 iterations.

## Slide 6: ESP32-C3 Rotate Right
Rotating the bits to the right requires an extra step, as shown in Listing 9.5. Line 5 performs an "and immediate“ operation placing a 1 or 0 into register a1. This example also illustrates that you can work with unused argument registers as temporary registers. Line 6 shifts that result in a1 up to bit 31. Then the argument value in a0 is shifted right (logical) one bit in line 7. Finally, the bit saved in a1 is or-ed into register a0 (line8) and then returned.
Program for rotate_right() function,
~/riscv/repo/09/ror/main/ror.S.
The main program to test rotate_right(),
~/riscv/repo/09/ror/main/main.c.
Modify , code in main.c
Add, #include <inttypes.h>
printf("rotate_right(0x%08" PRIx32 ") returned 0x%08"
PRIx32 "\n", bits, rol);
Build, flash and monitor the program :
Notes: exercise, create a RV64 version of the same to be run
under QEMU. There is one minor change needed for
ror.S ?

## Slide 7: Pseudo Opcodes
The "not" opcode is the same as the familiar one’s complement (~) operator in C. The "neg" opcode produces a two's complement value by subtracting rs from zero. The "negw" is for the RV64 and larger platforms to treat a 64-bit value initially as a 32-bit value and then sign extend the result.

## Slide 8: Unsigned Multi-precision Arithmetic
Multi-precision unsigned program,
~/riscv/repo/09/multipu/main/multipu.S.
Main driver program ~/riscv/repo/09/multipu/main.c.
Build, flash and monitor the program to see the results:
$ cd ~/riscv/repo/09/multipu
$ idf.py build
Unsigned Overflow Testing for unsigned overflow is equally simple, since all that is required is to see if a carry occurred out of the high order word.

## Slide 9: Signed Multi-precision Arithmetic
Signed arithmetic handles the carry precisely the same way. When adding the low order words, simply test if the result of the sum is less than either of the operand words.
Signed Overflow
Program ~/riscv/repo/09/multips/main/ovflow.S.
Main driver program
~/riscv/repo/09/ovflow/main/main.c.
$ cd ~/riscv/repo/09/ovflow
$ idf.py build

## Slide 10
Modiy the main.c code
In the output, the first example retains the original sign after the sum (result 0x7FFFFFFF). However, in the second sum, we see that the sign changed (result 0x8000002C) and the function s32ovf() correctly identifies it as an overflow. The third test had inputs of different signs and the result remains ok. The final test results in an overflow, which is correctly identified.
Output

## Slide 11
RV64 Signed Overflow
Main driver program: ~/riscv/repo/09/ovf64/qemu64/main.c.
Compile and run the program in Fedora Linux as follows:
$ cd ~/riscv/repo/09/ovf64/qemu64
$ gcc -g addi64.S main.c
$ ./a.out
We see that the addi64() function performs the 64-bit addition and returns the correct overflow status for the two tests (first two lines of output). The last four lines of output are the result of testing neg64(). From the output shown, it is evident that the results of these tests are correct and that the one overflow case was identified.

## Slide 12: Thank You !