## Slide 1
Presentation by Yi-Chih Tung
Chapter 10
Multiply / Divide

## Slide 2: Multiplication Operations
When you multiply a 32-bit value (multiplier) by another 32-bit value (multiplicand), you obtain a result (product) that is represented by up to 32+32 bits in length. Because of this, some architectures provide one opcode for producing a product in a register pair. RISC-V takes a different approach. It defines opcodes to produce only the low order word, or another to return the high order product word.
Integer multiplication and division are essential mathematic operations. Yet RISC-V defines these as an extension M, which permits vendors to create CPUs without this capability to save on cost. These operations can, of course, be performed in software but at the expense of CPU time. These added opcodes boost the overall performance of the CPU.

## Slide 3: Signed Multiplication
Multiplication can be performed as unsigned or signed integer operations. Unsigned multiplication is often used for C language subscripting operations within an array or matrix, where the first element is at subscript 0.
When multiplying signed numbers, the product's sign obeys the following relationships:
• a positive ⅹ positive → positive
• a positive ⅹ negative → negative
• a negative ⅹ positive → negative
• a negative ⅹ negative → positive

## Slide 4: Division Operations
When dividing a 32-bit number (dividend) by another 32-bit number (divisor), it produces a result (quotient) up to 32 bits in length. Dividing by 1 will do, this for example. Addition ally, when dividing integers, you may need the remainder. So, a division may be expected to produce both the quotient and remainder.
Signed Division
When dividing signed numbers, the quotient's and remainder's sign obeys the following rules:
• a positive ÷ positive → positive quotient, positive remainder
• a positive ÷ negative → negative quotient, positive remainder
• a negative ÷ positive → negative quotient, positive remainder
• a negative ÷ negative → positive quotient, negative remainder

## Slide 5
Opcode mul/mulu
The RISC-V integer multiplication opcode is "mul" or
"mulu" for signed and unsigned re spectively:
The destination register receives the lower XLEN bits of the product. To obtain the upper XLEN bits of the product, the "mulhs" (signed) or "mulhu" (unsigned) opcodes are available.
Opcode mulhs/mulhu
To obtain the upper XLEN bits of the product, use the "mulh" or "mulhu" opcodes for signed and unsigned respectively:
Optimized Multiply
To get the full XLEN+XLEN bit product, use the following back-to-back instructions for signed multiply, in this specific sequence:
The destination register rdh receives the high order product word while rdl receives the low order product word. Register rdh cannot be the same as rs1 or rs2 for the optimized operation. For unsigned products use the following sequence instead:
For the multiply to function optimally, the following rules must be observed:
1. The mulhs or mulhu opcode must occur first.
2. The mul or mulu opcode must immediately follow.
3. Source registers rs1 and rs2 must be provided in the same order for both instructions.
4. And the destination register rdh cannot be rs1 or rs2. Unsigned Factorial

## Slide 6: Unsigned Factorial
Exercise for the ESP32-C3 device, let's compute an unsigned factorial value of x! The ufact32() function computes the factorial without checking for overflow but is otherwise, designed to be as frugal as possible.
Unsigned factorial in: ~/riscv/repo/10/factorial/main/factorial.S.
Main program for ufact32() in file: ~/riscv/repo/10/factorial/main/main.c.
$ cd ~/riscv/repo/10/factorial
$ idf.py build
Modiy main.c
#include <inttypes.h>
printf("%2u ! => %" PRIu32 " 0x%08" PRIx32 "\n", ux,f, f);

## Slide 8
The hexadecimal value was printed on the right so that you can visualize the limit of this calculation (eight hexadecimal digits).
Can check this using the Linux bc command:
$ bc
The 12! result is indeed 479001600, but 13! Overflows 32-bits to the value 6227020800 (0x17328CC00).

## Slide 9
Opcode div/divu
Division is even more costly to evaluate than multiplication. It is therefore beneficial to have it included in the M extension. The following opcodes provide an operation that divides an XLEN-bit dividend value by an XLEN-bit divisor. Two opcodes provide for signed and unsigned division:
Opcode rem/remu
In addition to division, a remainder is often required. The "rem" and "remu" opcodes pro vide the remainder after dividing an XLEN-bit dividend value by an XLEN-bit divisor, for signed and unsigned numbers respectively:

## Slide 10
Optimized Divide
Algorithms frequently require both the quotient
and the remainder in a calculation. So why expend extra time performing the operation twice? Like the optimized multiply operation, RISC-V permits an optimized divide if the programmer issues the instructions as a sequence in a specific order.
Division By Zero
Division by zero has that mathematical quirk that there
is no defined answer. Some architectures raise an exception when this is attempted. The designers of RISC-V felt it best to simply specify the result of such an operation instead since it is easy to test for this condition.
For signed division by zero, the following results apply:
• x÷0→-1
• x% 0→0
For unsigned division, the following results apply:
• x÷0→2XLEN-1
• x% 0→x
Divide Overflow
Division of signed integer numbers also has the quirk
that an overflow is possible in one specific case. Like the
negate operation, the signed divide overflows when the
most negative number of XLEN bits is divided by a
negative one.
RISC-V defines the following results for overflow:
• 2XLEN/-1→2XLEN-1
• 2XLEN-1mod-1→0

## Slide 11: Safe Division
The example illustrates the function safediv(), which returns both quotient and remainder, as well as flags indicating a divide-by-zero and overflow conditions.
The safediv() function in file: ~/riscv/repo/10/safediv/main/safediv.S.
Build, flash and run the program on your ESP32-C3
as follows:
$ cd ~/riscv/repo/10/safediv
$ idf.py build
Modify main.c
#include <inttypes.h>
printf("%" PRId32 " / %" PRId32 " => %" PRId32 "
remainder %" PRId32 "; "
"divbyzero=%d, overflow=%d\n",
dividend, divisor, quotient, remainder,
divbyzero, overflow);

## Slide 12
In the resulting output, the first two lines report valid quotient and remainders with no divide-by-zero or overflow flags set. The third line does, however, report a divide-by-zero failure (and also confirms the quotient result of -1 and a remainder of 46, which was the dividend). The second to last line reported an overflow.
This is correct because a maximally negative 32-bit number (-2147483648) divided by -1, should be the positive value +2147483648, which cannot be represented by a signed 32-bit number.

## Slide 13: Greatest Common Divisor
Let's implement a function named gcd64(), which will calculate the greatest common divisor between two integers
Use under Fedora Linux (QEMU).
The function is based upon the following algorithm:
1. If a = 0 in GCD(a,b) then return b (GCD(0,b) = b).
2. If b = 0 in GCD(a,b) then return a (GCD(a,0) = a).
3. If b > a then swap a and b.
4. Otherwise, we compute r = a % b, to satisfy the equation a = b q + r.
5. Set a = b and b = r to e ectively call GCD(b,r).
6. Repeat from step 1.
The gcd64() function in
~/riscv/repo/10/gcd/qemu64/gcd64.S.

## Slide 14
Main driver program ~/riscv/repo/10/qemu64/main.c.
$ cd ~/riscv/repo/10/gcd/qemu64
$ gcc -g gcd64.S main.c
$ ./a.out

## Slide 15: Combinations
Let's compute a combination C(n,r) function such that out of n objects, determine how many unique samples of size r, can be obtained. This is calculated with the formula:
The nCr() function found in file
~/riscv/repo/10/nCr/qemu64/ncr.S.
Compile and run the test under Fedora Linux as follows:
$ gcc -g ncr.S main.c
$ ./a.out
Notes: With the use of the RISC-V M extension, the entire
computation was performed in hardware. The number of
registers available in a RISC CPU often permits optimal
execution.

## Slide 16: Summary
This chapter has shown the utility and use of the multiply and division operations provided by the RISC-V extension M. When this extension is not provided, execution time suers considerably because these operations must be performed in software.

## Slide 17: Thank You !